Molecfit Optical Depth Adaptation NOTES
## Introduction:
The plan is to execute lnfl and lblrtm prior to the cplmfit process. Thecalls for lnfl will be broken down to per wavelength range (as before) and per single molecule. The lblrtm will be broken down to per wavelength range (as before), per single molecule, and then per wavenumber subsection.

### Old System lnfl working directory structure

wdir_lnfl_range1:
TAPE1	-> Given (Soft link to gdas file)
TAPE5	-> Given (Generated by molecfit)
TAPE10	-> lnfl output
TAPE6	-> lnfl output
TAPE7	-> lnfl output
TAPE3	-> lnfl output (Required for lblrtm)
### New System lnfl working directory structure including molecule specific subdirectories
wdir_lnfl_range1:

H2O/:
TAPE1	-> Given (Soft link to gdas file)
TAPE5	-> Given (Generated by molecfit for H2O only)
TAPE10	-> lnfl output
TAPE6	-> lnfl output
TAPE7	-> lnfl output
TAPE3	-> lnfl output (Required for lblrtm)
O3/:
TAPE1	-> Given (Soft link to gdas file)
TAPE5	-> Given (Generated by molecfit for O3 only)
TAPE10	-> lnfl output
TAPE6	-> lnfl output
TAPE7	-> lnfl output
TAPE3	-> lnfl output (Required for lblrtm)
CH4/:
TAPE1	-> Given (Soft link to gdas file)
TAPE5	-> Given (Generated by molecfit for CH4 only)
TAPE10	-> lnfl output
TAPE6	-> lnfl output
TAPE7	-> lnfl output
TAPE3	-> lnfl output (Required for lblrtm)

### Old System lblrtm working directory structure
 Old system has toplevel directpry name generated for each iterative call and based on run, range and call number eg:

run_5_wdir_lblrtm_range_2_lblrtm_call_18

The subdirectory are then broken down into wavenumber subranges e,g:
wv_number_0:
TAPE3	-> Given (Soft link to lnfl TAPE3 file)
TAPE5	-> Given (Generated by molecfit)
TAPE10	-> lblrtm output
TAPE11	-> lblrtm output
TAPE12	-> lblrtm output
TAPE6	-> lblrtm output
TAPE9	-> lblrtm output
TAPE28	-> lblrtm output (Desired output)
wv_number_1:
(same as above)
The new system is called independently of iteration and can have a toplevel directory name similar to that of lnfl, i.e. one per range:
wdir_lblrtm_range_1
wdir_lblrtm_range_2

Then as with the new lnfl directory sturcture, the next level of subdirectories are molecule specific and then finally wavenumber subsection:

wdir_lblrtm_range_1:
H2O/
wv_number_0/
TAPE3,TAPE5,…,TAPE28
wv_number_1/
TAPE3,TAPE5,…,TAPE28
O3/
wv_number_0/
TAPE3,TAPE5,…,TAPE28
wv_number_1/
TAPE3,TAPE5,…,TAPE28
CH4/
wv_number_0/
TAPE3,TAPE5,…,TAPE28
wv_number_1/
TAPE3,TAPE5,…,TAPE28

After lblrtm has been successfully called in each work directory, the TAPE28 files can be parsed and and combined to produce optical depth profiles for each molecule per each range.

Vector Pair : OD([molecule],[range])[n], WN([molecule],[range])[n]

If the WN([molecule],[range])[n] vector is not independent of molecule, then interploation can be applied to generate OD vectors on the same wavelength range to produce the following vectors:

Vectors: OD([molecule],[range]) [m], WN[range])[m]

of the I have developed executable python scripts: lnlODA and lblrtmODA and placed them in the molecfit bin directory. These act as wrappers to lnfl and lblrtm respectively and parse TAPE5 files that molecfit produces and creates a TAPE3dir directory that contains Optical Depth files generated by usage of lnfl and lblrtm on single molecular data. For the remainder of this document I shall use the terms lnflODA and lblrtmODA and TAPE3dir to prevent confusion. However, the end goal is to rename lnfl and lblttm to lnfl_std and lblrtm_std respectively, whilst renaming lnflODA, lblrtmODA and TAPE3dir to lnfl, lblrtm and TAPE3 respectively. The reason for this is that molecfit would then be able to work with the newer executables and TAPE3 data format without the need to change molecfit code. This would be a good starting point for testing the new process. I will now explain lnflODA, lblrtmODA and TAPE3dir and how they can work with molecfit in more detail below.

## TAPE3dir
This directory will be the output of lnflODA and the input for lblrtmODA. Despite being a directory instead of a file, the operations that molecfit performs on moving and linking file TAPE3 will still work for a directory TAPE3dir. TAPE3dir will contains subdirectories for each molecule of interest each of which contains a TAPE3 file generated by lnfl for that molecule only. For example when the molecules of interest are CH4, O3 and H2O, the TAPE3dir structure will be as follows:

    TAPE3dir:
  /	|	\
CH4	O3	H20
 |	|	|
TAPE3	TAPE3	TAPE3

## lnflODA
A python executable script. This takes a TAPE5 from working directory (as generated by molecfit) as input and:
- Parses TAPE5 for list of molecules
- Creates a subdirectory for each molecule, eg CH4, H20 and O3 to be used as individual working directories for lnfl
- For each molecule, creates a modified TAPE5 that lists only that molecule and places the TAPE5 file into the relevant molecule subdirectory
- Creates a soft link to TAPE1 in the working directory to each molecule subdirectory
- For each molecule subdirectory, cd to that directory then call lnfl (this could be done in parallel)
- Creates a TAPE3dir with molecule subdirectories each of which has a soft-link to the associated TAPE3 generated by lnfl.
Thus the working directory prior to execution will contain two files: TAPE1 (as soft-linked by molecfit); and TAPE5 (as generated by molecfit). After execution, the working directory will also contain molecule working subdirectories, eg CH4, O3 and H2O and TAPE3dir. Each molecule working subdirectory will house all the TAPE files needed for lnfl execution and a TAPE3 file that lnfl produced. For example the CH4 working directory will contain:
- TAPE1 (soft-link from ../TAPE1)
- TAPE5 (parsed from ../TAPE5)
- TAPE3 (generated by lnfl)
With the CH4,O3,H2O example, TAPE3dir would consist of the following:
- Physical subdirectories: CH4, H2O and O3
- Soft link file: TAPE3dir/CH4/TAPE3	linked to ../../CH4/TAPE3
- Soft link file: TAPE3dir/O3/TAPE3	linked to ../../O3/TAPE3
- Soft link file: TAPE3dir/H2O/TAPE3	linked to ../../H2O/TAPE3

## lblrtmODA
An executable python script with 2 stages:
- lblrtm_GenODFiles	Generate Optical Depth files for each molecule
- lblrtm_MrgODFiles	Merge Optical Depth files with specific ratios

Firstly, lblrtmODA will first check if molecule specific Optical Depth files have been generated in the TAPE3dir directory. If not then it will call on lblrtm_GenODFiles to do so. Secondly, lblrtmODA will call on lblrtm_MrgODFiles to combine the Optical Depth data in appropriate ratios and to generate a TAPE28 file that Molecfit can read.
### lblrtm_GenODFiles
- Parses the TAPE5 file in the working directory and generates a single molecule specific version with modified output instructions to produce Optical Depth files.
- Places the molecule specific TAPE5 into the relevant molecule subdirectory of TAPE3dir
- For each molecule subdirectory, cd to that directory then call lblrtm (this could be done in parallel)
### lblrtm_MrgODFiles
Parse the TAPE5 file in the working directory for the abundance values for each molecule.
Merge the OD values in the TAPE3dir accordingly to generate a TAPE28 file that molecfit can read. Note, that whilst the governing body of this script is python, the actual merging of the optical depth data is being executed in fortran using lblrtmio library. This ensures expedience and precision.

## Where I am at:
- I am still working on the correct translation of TAPE5 files from multi molecules to single molecules. Currently I am using TAPE5 files generated by molecfit when specifying one molecule at a time. This just needs a little more exploration/understanding of the TAPE5 formats for both lnfl and lblrtm.
- Need to generate a TAPE28 file from the merged data of the OD files that molecfit will recognise.